## Slide 1
Flash → Multi-PE → Stream on AutoSA 64³ GEMM
DeepSeek-v4-flash · Alveo U280 · 3.33 ns · scored kernel is Stream · gate: Stream ≤ Rank1 × 1.02
Benchmark | Flash | Multi-PE | Stream | Rank1 | vs Rank1
mm | 24,745 1 PE · 80 DSP · II=1 | 13,160 16 PE · 352 DSP · II=1 | 4,299 16 PE · 352 DSP · II=1 | 4,228 16 PE · 320 DSP | +1.7%
mm_hcl* | 33,357* 1 PE · 40 DSP · II=8 | 12,770 32 PE · 384 DSP · II=1 | 4,294 32 PE · 320 DSP · II=1 | 4,230 32 PE · 320 DSP | +1.5%
mm_hcl_intel | 35,085 1 PE · 48 DSP · II=4 | 17,485 16 PE · 352 DSP · II=1 | 4,292 16 PE · 320 DSP · II=1 | 4,226 16 PE · 320 DSP | +1.6%
mm_int16 | 4,509 1 PE · 64 DSP · II=1 | 8,626 32 PE · 64 DSP · II=1 | 4,280 32 PE · 64 DSP · II=1 | 4,219 32 PE · 64 DSP | +1.4%
mm_catapult* | 32,916* 1 PE · 24 DSP · II=8 | 17,688 8 PE · 96 DSP · II=1 | 8,351 8 PE · 96 DSP · II=1 | 8,286 8 PE · 96 DSP | +0.8%
mm_intel† | 29,457 1 PE · 64 DSP · II=4 | 10,750 32 PE · 704 DSP · II=1 | 4,308† 32 PE · 640 DSP · II=1 | 4,178 32 PE · 640 DSP | +3.1%
mm_getting_started† | 12,588 1 PE · 352 DSP · II=1 | 10,750 32 PE · 704 DSP · II=1 | 4,307† 32 PE · 640 DSP · II=1 | 2,194 32 PE · 640 DSP | +96%
II = compute-loop pipeline initiation interval (pe_kj / accumulate / flattened i×j). Flash has no PE array (PE = 1).
* Flash returned no code; number is the phase-B seed. † Stream still serializes two i-tiles inside DATAFLOW (II=1 on pe_kj, latency ≈ 2× rank1 for getting_started).
mm is the Aug 23 gf cell (4,299), not the Aug 18 nav_n 4,285. SIMD: mm/hcl_intel 4 · hcl/int16 2 · intel/getting_started 4 · catapult 4.

## Slide 2
Same table, expanded columns · cycles / PE / DSP / II
U280 3.33 ns csynth · copy this grid into a paper or spreadsheet
Benchmark | Flash |  |  |  | Multi-PE |  |  |  | Stream |  |  |  | Rank1 |  |  | vs Rank1
 | cyc | PE | DSP | II | cyc | PE | DSP | II | cyc | PE | DSP | II | cyc | PE | DSP | 
mm | 24,745 | 1 | 80 | 1 | 13,160 | 16 | 352 | 1 | 4,299 | 16 | 352 | 1 | 4,228 | 16 | 320 | +1.7%
mm_hcl* | 33,357* | 1 | 40 | 8 | 12,770 | 32 | 384 | 1 | 4,294 | 32 | 320 | 1 | 4,230 | 32 | 320 | +1.5%
mm_hcl_intel | 35,085 | 1 | 48 | 4 | 17,485 | 16 | 352 | 1 | 4,292 | 16 | 320 | 1 | 4,226 | 16 | 320 | +1.6%
mm_int16 | 4,509 | 1 | 64 | 1 | 8,626 | 32 | 64 | 1 | 4,280 | 32 | 64 | 1 | 4,219 | 32 | 64 | +1.4%
mm_catapult* | 32,916* | 1 | 24 | 8 | 17,688 | 8 | 96 | 1 | 8,351 | 8 | 96 | 1 | 8,286 | 8 | 96 | +0.8%
mm_intel† | 29,457 | 1 | 64 | 4 | 10,750 | 32 | 704 | 1 | 4,308† | 32 | 640 | 1 | 4,178 | 32 | 640 | +3.1%
mm_getting_started† | 12,588 | 1 | 352 | 1 | 10,750 | 32 | 704 | 1 | 4,307† | 32 | 640 | 1 | 2,194 | 32 | 640 | +96%
* Phase-B seed (flash returned no code). † Inner i-tile loop still inside DATAFLOW tasks — stream retry job 2634808. Gate IN if Stream ≤ Rank1 × 1.02.
PE at Flash = 1 (no array). Rank1 II = 1 on all seven kernels.