## Slide 1
Closing the AutoSA matrix-multiply gap with an LLM HLS agent
Kernel autosa_mm (I = J = K = 64, float) · Alveo U280, 3.33 ns, Vitis HLS 2023.2 Reference: AutoSA rank-1 HLS (paper Fig. 11a Design 1 class), not ChatHLS Agent: DeepSeek-v4-flash · seed: plain.cpp, not stripped kernel0
Supervisor briefing · answers to the requested study · 8 September 2026 Metrics: latency min, latency max, DSP. Interval and HLS estimated clock are not comparison metrics. Middle stage is a 16×4 compute rewrite (hide load-store), not AutoSA design-space search.
Notes: Open with two comparisons. Do not put 940 next to 4228. Do not say DSE.

## Slide 2
Held fixed for the study
Experimental protocol
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
2 / 26
Item | Value
Kernel / size | autosa_mm, I = J = K = 64, typedef float data_t
ABI | extern "C" void autosa_mm(A[I][K], B[J][K], C[I][J]) — B stored B[j][k]
Gold | C = A · B from zero. Kernel must not treat DRAM C as an accumulate input.
Device / tool | xcu280-fsvh2892-2L-e · Vitis HLS 2023.2 · clock 3.33 ns
Seed | related_work/.../autosa_mm/plain.cpp. Not stripped AutoSA kernel0.
Reference | AutoSA rank-1 4228 cycles / 320 DSP (Design 1, 1-D along i). Not ChatHLS.
Agent | DeepSeek-v4-flash. Cosim off except where named.
Reported metrics | Latency min, latency max, DSP. Do not quote interval or estimated clock.
Notes: Trap: an older plainseed_stream run generated AutoSA rank-1 and stripped pragmas. This study does not use that seed.

## Slide 3
The questions were two
Two comparisons — do not mix them
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
3 / 26
Comparison 1 · iso-compute
Comparison 2 · spend DSP
16 PE × SIMD 4 ≈ 320 DSP
Same MAC budget as AutoSA rank-1.
AutoSA rank-1: 4228 / 320
Agent stream (empty skills JSON): 4216 / 320
Agent stream (90-skill mmflow): 4292 / 320
Aug 18 first locked stream: 4285 / 320
Fair architecture-class comparison.
Pass band used later: ≤ ×1.02 (4312).
Flash allowed to spend U280 DSP (9024)
Not a fair beat of 4228. ~17× DSP.
Champion: 940 / 5344 (csynth)
Cosim PASS 1071. Kernel type: no.
Do not put 940 or 871 next to 4228.
871 csynth / 1224 cosim is fused I/O,
not the champion and not this comparison.
Notes: If one slide mixes 940 and 4228 as a speedup, the rest of the talk is noise.

## Slide 4
17 August · what was held, what was not
1. Original request: one kernel, gap vs rank-1
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
4 / 26
Held fixed | Not held fixed | Not done
Top name, ABI, B layout J×K, U280, 3.33 ns, gold-from-zero TB, iso-compute 16×4 on comparison 1 | Internal nest. Flash, compute rewrite, and stream each change the code. That is the method. | AutoSA array_part / space_time / simd search. We did not call AutoSA. We did not emit kernel0 / A_t16 / L2 FIFOs as the agent result.
What AutoSA automates, cloned as a plan (not the compiler)
(1) Many PEs that do not wait on one running total — compute rewrite, PE=16 SIMD=4 via post_flash_pe_recipe.py.
(2) Memory filling the next chapter while they work — stream rewrite: DATAFLOW + hls::stream, A private per PE, B forwarded, C drained.
Knobs for this mm were fixed at 16×4. We did not hunt them on the locked slide.
Disk still labels the middle stage dse. Slides say compute rewrite / hide load-store.

## Slide 5
Csynth latency min, cycles · naive 2 445 313 omitted from the plot (destroys scale)
Iso-compute path (comparison 1)
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
5 / 26
Chart: 
| Flash 90-skill | Compute rewrite | Enforcement | Stream +skills | Stream no JSON | AutoSA rank-1
Csynth latency min (cycles) | 139484 | 13160 | 12893 | 4292 | 4216 | 4228
Flash / compute / stream: frozen 20260830_mmflow. Enforcement: 20260829_123043. Rank-1: AutoSA 20260709_full21_dse resynth 3.33 ns. Aug 18 first locked stream (nav_n) was 4285 / 320; mmflow with-skills is 4292 / 320. Gap vs 4228: with-skills +64 cycles (+1.5%); empty-JSON stream −12 cycles (−0.3%). Wave1 pass band ≤ 4312.
Notes: 90-skill flash 139484 / 10 DSP is a legal kernel with almost no MAC parallelism. PE recipe + stream close rank-1.

## Slide 6
Comparison 1 · latency min–max and DSP
Pipeline stages (frozen mmflow unless noted)
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
6 / 26
Stage | Job | Latency min–max | DSP | Campaign
Phase B naive | Functional HLS, no opt pack | 2 445 313 | 50 | hls_synth__ref_baseline
Flash 90-skill | Legal kernel + generic HLS pack | 139 484 | 10 | 20260830_mmflow
Compute rewrite | 16×4 on-chip PEs, II=1 compute, LCST serial | 13 160 | 352 | 20260830_mmflow
Enforcement | Ping-pong DATAFLOW judged present | 12 893 | 320 | 20260829_123043
Stream | Hide load/store on that array | 4292 | 320 | 20260830_mmflow
Stream, empty JSON | Same PE recipe, skill_count=0 | 4216 | 320 | 20260902_mmns
AutoSA rank-1 | Published Design 1 class | 4228 | 320 | AutoSA inventory
Attribution at 320 DSP: PE recipe + stream skeleton, not the 90-skill dump. Empty JSON still closes rank-1.

## Slide 7
Requested pack-level, not skill 3 of 5 · same ABI, csim on, cosim off
2. Ablation: generic HLS vs enforcement vs systolic rewrite
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
7 / 26
Col | What was given | Latency | DSP | Result
1 | Generic HLS (90-skill flash) | 139 484 | 10 | Legal kernel, no PE array. Almost no MAC parallelism.
2 | Skills + ping-pong/DATAFLOW enforcement | 12 893 | 320 | Pragma present. Finish still load+compute+store. Overlap gate fail.
3a | Systolic: 90-skill + PE recipe + stream pack | 4292 | 320 | +1.5% vs 4228.
3b | Same PE recipe; skills JSON empty | 4216 | 320 | −0.3% vs 4228.
The PE recipe plus stream skeleton matter more than the 90-skill dump. Generic flash can emit a legal kernel with 10 DSP. Empty JSON still closes rank-1 if the compute-rewrite/stream path still instantiates 16×4.
Column 1 is not a PE-free baseline of the systolic path: it is the 90-skill flash kernel. Column 3b is the systolic PE recipe with the skill JSON emptied.

## Slide 8
Repair success = csim + legal csynth. No DSP / II judge until 3 September.
3. Why flash was II=4 / low DSP, and why later stages sat on it
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
8 / 26
Fact | Number / mechanism
Aug 18 flash | 149 082 cycles, 6 DSP, II=4 on k (scalar FP-add recurrence)
Frozen mmflow flash | 139 484 cycles, 10 DSP
Flash job definition | Legal, testbench-correct HLS with interfaces. Success = csim pass + csynth.
Why repair did not catch II=4 | Repair loops on compile / csim / csynth failure, not on II or DSP. An II=4 kernel synthesizes.
Compute rewrite after that flash | 13 160 / 352. Compute nest ~4816 at II=1. Remaining: sequential load ~4100 + store ~4100.
Wrong comparison | Measuring flash vs AutoSA 4228 is not iso-compute. Flash is not the PE array.
Section 8 (spend DSP) answers “flash itself must stop under-using DSP.” Multi-PE replaces the nest; it does not require flash II=1.

## Slide 9
array_part[16, 64, 32] · latency[1, 32] · simd[4] · 1-D along i · 4228 / 320 DSP
Tiling A. AutoSA rank-1 (Design 1 class)
Tile sizes from kernel0 / autosa-mm-rank1-tiles · not candidate 9
9 / 26
16 PEs in a chain (not a 2-D i,j or i,k mesh). PE p owns C row i0+p, all 64 columns, as local_C[64].
PE0
PE1
PE2
PE3
PE4
PE5
PE6
PE7
PE8
PE9
PE10
PE11
PE12
PE13
PE14
PE15
B forwarded PE p → PE p+1 each beat. SIMD-k = 4 independent a[s]·b[s], then one add into Crow. Reduction is the outer K-tile.
A (I × K = 64 × 64)
Live this step: 16 rows × 32 k (I-tile × K-tile)
4 I-tiles (c0 = 0…3). A unique from DRAM.
B (J × K, stored B[j][k])
Live this step: 64 × 32 (full J × K-tile) ping-pong on-chip
J is not coarse-tiled. B replay once per I-tile (4× DRAM B).
C (I × J = 64 × 64)
Live in the PE: 16 rows × 64 cols local_C[64] per PE
Drain C only on last k-group of K-tile 1. Gold from zero: no load_C.
Loop | Tiles | On-chip this step | I/O schedule
c0 (I) | 4 × 16 rows (i = 0–15, 16–31, 32–47, 48–63) | A 16×32; C 16×64 | A unique; B replayed each I-tile
c2 (K) | 2 × 32 k (k = 0–31 then 32–63) | B 64×32 ping-pong | Fill tile t+1 while PE consumes tile t (paper §6.3)
J | not coarse-tiled | full C row of 64 in each PE | Inner c6/c4 walk 32+32 j; drain after last K-tile
Notes: Candidate 9 is 2-D J×K tiles (array_part[64,32,32], ~1296 DSP). Do not present cand-9 as Design 1. Planned rank-1-shaped manual uses A 16×32, B 64×32, C 16×64 — different from the 940 champion.

## Slide 10
Comparison 1 · same 16×4 · 320 DSP · not the 940 kernel
Tiling B. Agent iso-compute stream vs enforcement
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
10 / 26
Hide load-store · 4292 / 4216 cycles · 320 DSP
Same PE geometry as Design 1: 16 PE × SIMD 4, 1-D along i.
Frozen mmflow parked full B on an I-strip (not rank-1 K-tiles of 32). Still closes 4228 at 320 DSP.
PE0
PE1
PE2
PE3
PE4
PE5
PE6
PE7
… PE8–PE15 · A private per PE · B forwarded · C drained
Packed FIFOs ap_uint<128> SIMD 4 floats / beat
Crow BIND_STORAGE ram_2p (not complete- partition on J)
Flatten pe_kj 1024 / 4096 beats Fuse Crow init + drain into MAC
One run ≈ slowest room. Load, 16 PEs, and store run together. Failures taught as avoid-rules: struct-of-float FIFOs 16 878 / 80 DSP; Crow complete-partition J → mux II=4; flatten-off refill 7162.
Enforcement DATAFLOW + ping-pong · 12 893 / 320
Judge: ping-pong DATAFLOW present on code and csynth.
Finish time is still the sum of rooms. Interval is not the result.
load ~4100 · DRAM A/B
↓ not hidden
compute ~4816 · 16×4, II=1
↓ not hidden
store ~4100 · DRAM C
Aug 23 overlap seed 8678 / 320: architecture gate fail (coarse tile overlap, inner stretches restart). Manual pe_pp 9640 / 352; pe_pp_plus 4688 / 352 — still not rank-1 I/O. mmflow overlap re-run Slurm 2789637: LLM timed out.
Notes: Stream is packed FIFOs + Crow ram_2p + flatten pe_kj, not the existence of a DATAFLOW pragma. Rank-1 interval ≈ latency because of K-tiles / B ping-pong / C drain.

## Slide 11
Comparison 1 · finish time, not interval
4. Stream is not DATAFLOW + ping-pong on multi-PE
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
11 / 26
Design | Latency | DSP | What actually overlapped
Enforcement (column 3) | 12 893 | 320 | Pragma shape. Finish time ≠ max(modules).
Aug 23 overlap seed (not mmflow) | 8678 | 320 | Coarse tile overlap. Architecture gate fail.
Manual pe_pp on mmflow multi-PE | 9640 | 352 | csim pass. Still not rank-1 I/O.
Manual pe_pp_plus | 4688 | 352 | csim pass. Still not the stream pack.
Stream hide load/store | 4292 / 4216 | 320 | Load, 16 PEs, store together. Packed ap_uint<128>, Crow ram_2p, flatten pe_kj 4096.
Rank-1 interval ≈ latency because of a systolic I/O schedule (K-tiles, B ping-pong, C drain), not because a DATAFLOW pragma exists. Do not quote enforcement interval 4553 as the result.

## Slide 12
Gate: agent latency ≤ rank-1 × 1.02 · campaign 20260825_wave1_aav_n_gf
5. Other AutoSA mm-family benches, ≤ 2% of rank-1
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
12 / 26
Bench | Agent | Rank-1 | DSP | vs ×1.02
autosa_mm (mmflow / noskills) | 4292 / 4216 | 4228 | 320 | pass
autosa_mm_hcl | 4294 | 4230 | 320 | pass 1.51%
autosa_mm_hcl_intel | 4292 | 4226 | 320 | pass 1.56%
autosa_mm_int16 | 4280 | 4219 | 64 | pass 1.45%
autosa_mm_catapult | 8351 | 8286 | 96 | pass 0.78%
autosa_mm_intel | 4525 | 4178 | 640 | fail 8.3% after retry 2789605 (ceiling 4261)
autosa_mm_getting_started | 4525 | 2194 | 640 | fail ~2× (rank-1 is two DATAFLOW tiles; agent I/PE=2)
Four of six wave1 benches pass. Intel compute-rewrite LLM timed out; stream still ran and promoted 4525 / 640. Not this round: cnn, lu, large_*, HBM.

## Slide 13
U280 has 9024 DSP. Rank-1 320 is iso-compute, not a fill of the chip.
6. Why 320 DSP
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
13 / 26
320 = 16 PE × SIMD 4 × ~5 DSP per float MAC at II=1. AutoSA chose that array for 64³ autosa_mm. The locked slide holds that point.
Array | Stage | Latency | DSP | vs 4228 / 320
16×4 (locked) | stream | 4292 | 320 | +1.5%
16×4 | stream, empty JSON | 4216 | 320 | −0.3%
32×8 20260830_mm32x8 | compute rewrite | 9782 | 1344 | more silicon, still sequential I/O
32×8 | stream | 4583 | 1280 | worse than 16×4 stream (I/PE=2, pe_kj=512 × two tiles)
Family C iso-DSP 32-PE | io4_8x4_s8_k32_j64 | 2245 | 1280 | misses AutoSA cand 9 ≤1846 at ~1296 DSP
Family C selected | io4_16x8_s8_k32_j64 | 1571 | 5120 | faster only by oversubscribing DSP
AutoSA exhaustive candidate 9 (2-D, not Design 1) is 1846–2161 / ~1296 DSP. Candidate 5 is 2033–2656. Paper Design 5 ≈ cand 9. Efficiency vs cand 9 is not closed. P&R / bitstream later.

## Slide 14
Transfer test: kernel-independent INTERFACE / PIPELINE / UNROLL / PARTITION / burst / LCST · comparison 1 flash
Skill pack 1. Generic HLS
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
14 / 26
skills_ii_target_miss_solutions_added(90skills).json (123 entries) + overlay flash_no_RMW_m_axi_skill_entries.json (33). Tagged kernel-independent.
Family | Exemplar skill id | One-line role
Burst / INTERFACE | axi-burst-widening-512, axi-burst-coalescing-narrow-safe | 512-bit m_axi widening; keep scalar pointer ABI
PIPELINE | prompt-pipeline, hls-pipeline-hot-loop-achieve-ii | Pick the hot loop; resolve II; not pragma-only
UNROLL | prompt-unroll, hls-unroll-independent-loop | Unroll independent loops after independence is proven
PARTITION | partition-cyclic-on-port-conflict | Bank local arrays to match unroll / pipeline ports
LCST staging | hls-pipeline-stage-global-memory, local-axi-staging-for-ii | Stage off m_axi before compute
No RMW overlay | avoid-no-rmw-m_axi-direct, hls-load-compute-store-no-rmw-m_axi | No m_axi accumulate; distinct gmem bundles
Contamination (transfer test fails): hls-baseline-load-compute-store-gate and hls-doublebuffer-load-compute-store encode PE_BLK ∈ {16,32,64}, 64×64 float LANES=16, and GEMM ping-pong buf[2]. That is not kernel-independent. This kernel: mmflow flash 139 484 cycles / 10 DSP. Legal. No 16×4 array. Not a systolic pass.
Notes: Classify by transfer, not filename. Mixing this pack into flash does not invent PEs.

## Slide 15
gemm_flatten_v1 + post_flash_pe_skill_entries.json + post_flash_pe_recipe.py · comparison 1 compute rewrite
Skill pack 2. GEMM-family (not AutoSA, not systolic I/O)
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
15 / 26
File on disk is still named post_flash_dse_pe_skill_entries.json. Slides: compute rewrite. IDs below are the file ids.
Skill id | Role
hls-gemm-static-nest-flatten-and-k-partition | Flatten i/k/j on a static nest; partition K so unrolled MACs have ports
hls-avoid-serial-fp-acc-under-full-k-unroll | Reject a single FP acc after claiming full-K unroll
hls-avoid-pipeline-innermost-only-goal-on-gemm | Innermost-only PIPELINE is not the GEMM pass
hls-avoid-outer-sequential-gemm-after-inner-pipeline | Do not leave i sequential after an inner II=1
hls-dse-gemm-multi-pe-latency-hiding | Rewrite compute nest into row PEs; pipeline independent j; keep LCST ABI
hls-dse-gemm-simd-k-adder-tree | SIMD-k=4 unrolled adder tree; pipelined loop is j, not k
hls-dse-partition-match-pe-simd | Crow complete on PE dim; A cyclic PE×SIMD; B cyclic SIMD on K
avoid-dse-k-recurrence-on-single-c | Reject k-loop recurrence on one C element (II=4, DSP~3–8)
hls-dse-pick-pe-simd-for-kernel | Read kernel.h + recipe. autosa_mm default 16×4; not a search
This kernel: compute rewrite 13 160 / 352 DSP. Compute nest ~4816 at II=1. Remaining latency is sequential load ~4100 + store ~4100. Recipe for autosa_mm is PE=16 SIMD=4 (post_flash_pe_recipe.py), not a design-space search.
Notes: Never say DSE. The PE recipe is fixed for the locked slide.

## Slide 16
post_flash_stream_pe_io_skill_entries.json (6 skills) · AutoSA I/O plan, not kernel0 · comparison 1
Skill pack 3. Systolic / hide load-store
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
16 / 26
Skill id | Role
hls-stream-pe-array-dataflow | PE_NUM mm_pe tasks under DATAFLOW; packed ap_uint FIFOs; Crow ram_2p; flatten pe_kj; fuse init/drain
hls-stream-io-overlap-dram | load_A / load_B / store_C as INLINE-off DRAM tasks; compute never touches m_axi
hls-stream-b-systolic-forward | Packed vec4_bits along the PE chain; always forward; drain_B consumes fifo_B[PE_NUM]
hls-stream-match-pe-pack-to-data-t | Pack SIMD as ap_uint<pack_bits>; float 16×4 → ap_uint<128>
hls-stream-tile-loop-around-dataflow | If I/PE>1, wrap DATAFLOW in the top i-tile; do not loop tiles inside mm_pe
avoid-stream-shared-local-abc | Reject shared on-chip A/B/C across DATAFLOW tasks; reject kernel0 clone
autosa_mm: PE_NUM=16, SIMD=4, pe_kj = (K/SIMD)×J = 1024 beats per I-strip, 4096 across four I-strips. Crow BIND_STORAGE ram_2p — never complete-partition J. This kernel: stream 4292 / 320 (90-skill mmflow) or 4216 / 320 (empty JSON, same PE recipe). Failures taught here: struct-of-float FIFOs 16 878 / 80; Crow complete-partition J → II=4; flatten-off 7162.
Notes: This pack is hide load-store on the 16×4 array. Mixing it into flash does not invent PEs.

## Slide 17
post_flash_overlap_pe_skill_entries.json (3 skills) · C2HLS_ENFORCEMENT · comparison 1 · not rank-1
Skill pack 4. Overlap / ping-pong PE
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
17 / 26
Skill id | Role
hls-overlap-fuse-crow-init-drain | Delete init_pe_j / wb_pe_j. First k-group writes; last k-group writes C. Same 16×4 MAC.
hls-overlap-pingpong-dataflow-on-pe-array | INLINE-off load_tile / compute_tile / store_tile. Outer i-tile wraps DATAFLOW. buf[2] A/C. Keep one compute_tile.
avoid-overlap-stream-pe-fifo-pack | Reject mm_pe + packed FIFO chain in this ablation. That is pack 3, already measured.
Judge: ping-pong DATAFLOW present on code and csynth (20260829_123043). Finish time 12 893 / 320 DSP — still load + compute + store. Overlap gate fails. Aug 23 overlap seed 8678 / 320: architecture gate fail (coarse tiles, inner stretches restart). A DATAFLOW pragma is not hide load-store. Rank-1 interval ≈ latency because of K-tiles, B ping-pong, and C drain.
Notes: Do not quote enforcement interval as the result. This column is not the systolic pass.

## Slide 18
flash_onchip_wide_gemm_skill_entries.json · PACKAGED_SKILLS_ONLY=1 · comparison 2 · not mixed into the 90-skill dump
Skill pack 5. On-chip spend-DSP
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
18 / 26
Skill id | Role
hls-onchip-stage-when-fits | Stage all of A and B; compute into C_local; never touch m_axi in compute. 64³ float fits.
hls-onchip-axi-512-three-bundles | gmem0/1/2, max_widen_bitwidth=512, LANES=16. Load/store trip ≈ 256, not 4096
hls-onchip-write-once-affine-c | Nested affine i / j+=PE_BLK. C_local[row][j0+p]=dot. No g>>k, no C RMW
hls-onchip-flatten-c-output-groups | One II=1 pipeline over I×(J/PE_BLK) groups. PE_BLK 16/32/64 after II=1
hls-onchip-full-k-unroll-adder-tree | Full UNROLL k into partial sums then a tree. Not a serial FP acc
hls-onchip-partition-match-unroll | A_local complete on K; B_local enough for PE_BLK; C_local complete on J group
avoid-onchip-dataflow-when-io-matches-compute | Reject DATAFLOW/ping-pong when compute ≈ 512-bit load window. 940 = max(A,B)+compute+store
avoid-onchip-kernel0-systolic | Keep autosa_mm ABI. Do not emit kernel0 / L2 FIFOs / mm_pe chain
Champion class: 940 / 5344, Cosim PASS 1071. Nested i / j+=LANES; two independent load modules. Fusion of A+B in one linearized-t loop is a failure mode (871 csynth / 1224 cosim) — not the champion, not comparison 1. JSON on disk also has later entries (avoid-onchip-fused-ab-lockstep, avoid-onchip-dsp-over-u280, row-uf, K-tile under DSP cap). Distilled 8 above are the 940-class pack.
Notes: Never put 940 next to 4228. Keep this pack out of the 90-skill dump and frozen mmflow.

## Slide 19
Comparison 2 · flash-only · not a fair beat of 4228
8. Flash must stop under-using DSP — one change per step
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
19 / 26
Chart: 
| min DSP 500 | +512-bit I/O | +write-once C | +PE_BLK=16
Csynth latency (cycles) | 9423 | 2760 | 1261 | 940
Step (one change) | Campaign | Latency | DSP | Then the report said
DSP floor 500 | …_dsp500_20260904_085931 | 9423 | 1344 | More MACs. Load/store still ~4k. LCST.
512-bit A/B/C, LANES=16, gmem0/1/2 | …_wideio_20260904_100437 | 2760 | 636 | I/O ~258. Compute 2099, Final II=4 (g>>k + C RMW).
Affine i, j+=PE; C_local=dot | …_computeii_20260904_120524 | 1261 | 2672 | Compute II=1.
PE_BLK=16 | …_pe16_20260904_131622 | 940 | 5344 | Two load modules. Type no. Cosim PASS 1071.
Ladder ends at PE_BLK=16. j-tile ping-pong and LLM tile-pp were worse (not shown).

## Slide 20
Comparison 2 · PE_BLK=16 · 5344 DSP · do not place beside 4228
Tiling C. Spend-DSP champion is not systolic tiles
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
20 / 26
Champion · nested i / j += LANES · 940 csynth / 1071 cosim
Not Design 1. No K-tiles. No B ping-pong. No mm_pe FIFOs. Full A, B, C staged on-chip (64³ float fits).
Nested load: for i … for j += LANES=16. Two independent load functions (separate stall domains).
load_A 259 cycles FF 540
load_B 258 cycles started together
max(259, 258) then
compute_blocks 340 · PE_BLK=16 · full-K adder tree · 5344 DSP
store_C 260 · WREADY in-loop; BVALID at parent
940 ≈ max(259, 258) + 340 + 260. Pipeline type: no. AXI 512-bit, three bundles, latency=32.
Failure mode · fused linearized-t load · not the champion
8-skill 7-turn 20260906_104733: 871 csynth / 5088 DSP, Cosim PASS 1224.
A and B in one II=1 loop over linearized t. Csynth priced lockstep II=1; RTL stalls if either gmem0 or gmem1 RVALID/ARREADY is 0.
one fused load_ab loop linearized t ~132 k FF in load vs champion load_A 540 FF
store waits BVALID inside the pipeline Cosim 1224 > champion Cosim 1071
Repro 20260906_123340: 1002 / 5344, split load_a/load_b, still linearized t — not nested i / j+=LANES. Fusion is model invention, not instructed. Do not put 871 on the 4228 slide.
Notes: j-tile ping-pong was worse (not shown). Champion remains 940. DSP 5344 = 59% of 9024, 177% of one SLR — allowed on comparison 2.

## Slide 21
Report: autosa_mm_csynth.rpt · 4 Sep 2026 15:33 · Vitis HLS 2023.2 · comparison 2
Latency per module — PE_BLK=16 champion (csynth)
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
21 / 26
Instance (csynth) | Module | Latency min–max | Pipeline type | DSP | FF
grp_…_load_A_rows_load_A_cols_fu_17020 | Pipeline_load_A_rows_load_A_cols | 259–259 | no | 0 | 540
grp_…_load_B_rows_load_B_cols_fu_17091 | Pipeline_load_B_rows_load_B_cols | 258–258 | no | 0 | 131 110
grp_…_compute_blocks_fu_21194 | Pipeline_compute_blocks | 340–340 | no | 5344 | 615 512
grp_…_store_C_rows_store_C_cols_fu_25422 | Pipeline_store_C_rows_store_C_cols | 260–260 | no | 0 | 2668
autosa_mm (kernel) | — | 940–940 | no | 5344 | 765 008
940 ≈ max(259, 258) + 340 + 260 · load A and load B are two modules, started together
Total resources (same report): BRAM_18K 90 · DSP 5344 · FF 765 008 · LUT 346 116 · URAM 0. Available device DSP 9024 (59%). Available SLR DSP 3008 (177% of one SLR) — allowed because comparison 2 asked for device DSP, not iso-320.
Cosim: artifacts/pc2/manual_pe16_tile_pp/cosim_pe16.json · PASS 1071 cycles, gold match. Target clock 3.33 ns; estimated clock is not a comparison metric.
Notes: Quote latency min/max 940 and DSP 5344. Do not quote interval 941 or estimated 2.431 ns as the result.

## Slide 22
Csynth unless Cosim is named · keep the two comparisons in separate columns
Module-level latency across designs
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
22 / 26
Design | Comparison | Modules (cycles) | One-call finish
Compute rewrite 13 160 / 352 | 1 (iso-320) | compute ~4816 II=1; load ~4100; store ~4100 (serial LCST) | sum: load + compute + store
Enforcement 12 893 / 320 | 1 | DATAFLOW pragma present; rooms still sequential | still load+compute+store; overlap gate fail
Stream 4292 / 4216 / 320 | 1 | load, 16 PEs, store overlapped; flatten pe_kj 4096 | ≈ slowest room (hide load-store)
AutoSA rank-1 4228 / 320 | 1 | K-tiles, B ping-pong, C drain; interval ≈ latency | systolic I/O schedule, not a pragma
PE_BLK=16 940 / 5344 | 2 (spend DSP) | load_A 259, load_B 258, compute 340, store 260 | max(A,B)+compute+store; Cosim 1071
Fused 8-skill 871 csynth / 5088 | 2 (not champion) | fused A+B lockstep; store BVALID in-loop | Cosim PASS 1224 — not 871
Do not call 871 the champion. Csynth priced fused II=1; RTL did not. Independent load modules (259 ∥ 258) are the 940 I/O shape.

## Slide 23
Not step 5 of the spend-DSP ladder · more than one code choice moved
Distilled 8-skill pack — a separate question
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
23 / 26
Run | Csynth | Cosim | I/O shape
8-skill, 7-turn, 20260906_104733 | 871 / 5088 DSP | PASS 1224 | Fused load_ab, linearized t. RTL stalls if either RVALID is 0.
8-skill, 7-turn, 20260906_123340 | 1002 / 5344 DSP | not run | Split load_a / load_b, still linearized t, not nested i, j+=LANES.
PE=16 champion (ladder endpoint) | 940 / 5344 DSP | PASS 1071 | Nested i / j+=LANES. Two load modules. Store WREADY only.
Pack: flash_onchip_wide_gemm_skill_entries.json, PACKAGED_SKILLS_ONLY=1, judges MIN_DSP=500 and PE_BLK=16. Not mixed into the 90-skill dump or frozen mmflow.
Why the LLM fused A and B: the prompt says latency = max(load_A,load_B)+compute+store and “overlapping A/B loads is enough,” and item 6’s trip target is one ~256-cycle load loop. Ignore FLASH item 5 kills DATAFLOW ping-pong, not dual-issue in one loop. Fusion is a reading of overlap, not a hard forbid being ignored.

## Slide 24
Iso-compute path · DSP as II proxy on this kernel
9. Stream failures that became avoid-rules
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
24 / 26
Attempt | Cycles | DSP | Failure
Struct-of-floats FIFOs | 16 878 | 80 | Four serialized float reads, II=4
Packed ap_uint<128> only | 18 607 | 80 | Still II=4
Crow complete-partition on J | same class | 80 | mux_case_0 FP recurrence, II=4
Crow ram_2p, flatten-off pe_k0 | 7162 | 320 | 16 k-tiles × 4 i-tiles refill of depth ~35
Flatten pe_kj 1024/4096, fuse init/drain | 4285 then 4292 | 320 | Aug 18 then frozen mmflow
DSP as II proxy on this kernel: 80 DSP ≈ 16 PEs × ~5 at II=4. 320 DSP ≈ 16 × 20 at II=1.

## Slide 25
As requested, not as a hedge
10. Limits and open items
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
25 / 26
Item | Status
Csynth + csim | Done on all quoted iso-compute numbers
Cosim | Off for mmflow / wave1 / ablation. On for PE=16 champion (1071 PASS) and fused 8-skill kernel (1224 PASS)
Bitstream / P&R / extra HBM | Not done
One model | DeepSeek-v4-flash
Clone AutoSA compiler / emit kernel0 as agent result | Not the method
Iso-compute vs rank-1 Design 1 | Closed: 4216–4292 vs 4228 at 320 DSP
Wave1 2% | 4/6 pass; intel and getting_started fail after retry
Efficiency vs cand 9 (1846 / ~1296 DSP) | Not closed. Needs K-tile + L1/L2 I/O, not more PEs
Frozen artifacts | Do not overwrite 20260830_mmflow, 32×8, family C first campaign, Aug 18 / Sep 2 briefs

## Slide 26
One kernel · two comparisons · one variation per step on spend-DSP
What to take from the study
c2hls · autosa_mm vs AutoSA rank-1 · U280 3.33 ns · Vitis HLS 2023.2
26 / 26
1
Iso-compute is closed at Design 1 class.
4216–4292 vs 4228 at 320 DSP. Empty skills JSON still closes if the PE recipe + stream skeleton remain.
2
Generic HLS skills are not the systolic pass.
90-skill flash 139 484 / 10 DSP is a legal kernel with almost no MAC parallelism. Enforcement DATAFLOW+ping-pong is 12 893, not rank-1 I/O.
3
Stream ≠ a DATAFLOW pragma.
Packed ap_uint<128>, Crow ram_2p, flatten pe_kj 4096, A private, B forward, C drain.
4
Rank-1 tiles are 16×32 on I×K, J not coarse-tiled.
array_part[16,64,32], 4 I-tiles, 2 K-tiles, B 64×32 ping-pong, C drain on last K-tile. Frozen agent stream parked full B; still 4292.
5
Spend-DSP is a different experiment.
940 ≈ max(259,258)+340+260 at 5344 DSP. Cosim 1071. Not a fair beat of 4228. 871 csynth is not the RTL finish time.
6
Cand-9 efficiency is not closed.
1846–2161 / ~1296 DSP needs K-tile + L1/L2 I/O, not more PEs.